## Slide 1: LMDCZ-AFD project: Regional 3D CROCO simulations
LMDCZ workshop, 12-14 April 2017 Ho Chi Minh City, Vietnam
Patrick Marchesiello
IRD, CARE Lab,
HCMC University of Technology

## Slide 2
Tidal and
frontal currents
Winter winds and waves
River discharge
Summer winds and waves
Coastal ocean forcing is complex: waves, tides, wind and density driven currents
Tidal range and currents larger on East coast (3.5 m) than West coast (1m).
Same for waves

## Slide 3: Shelf and nearshore processes
River input
Innershelf (10km)
Nearshore (1km)
Resuspension
Transport
Deposition
Mobile mud belt
Delta front

## Slide 4: Ocean modeling systems
WAVES
Hs, T, Dir
BOTTOM LAYER
Bottom stress due to waves and currents
SEDIMENTS
Sediment and bed properties
SEDIMENT model
Deposition, erosion, suspended and bedload transport, bed evolution
OCEAN CIRCULATION
Wave-averaged
U,V, Tracers equations
WAVES
Boundary forcing and breaking parameters
DATA
ATMOSPHERE

## Slide 5: CROCO: a community 3D coastal modeling system based on ROMS
Full 3D model with active and passive tracers
Wave-current interactions
Sediment model (cohesive and non-cohesive)
Optimized for parallel computers and high resolution problems

## Slide 6
Configuration

## Slide 7
Domain size |  | Covers whole LMDCZ system
Horizontal resolution |  | 500 m (374x727pts)
Vertical resolution |  | 10 levels (terrain following)
Topography |  | SIWRR data (estuaries, nearshore area) + GEBCO_2014 at 30” (1km)
River forcing |  | Discharge and SSC at Can Tho and My Thuan from SIWRR station data
Tidal forcing | U,V, SSH | OSU TPXO8 global solution at 1/30° (~3 km)
Subtidal forcing | U,V, SSH, T, S, SSC | ECCO V2 reanalysis ¼° 3-daily
Air-sea forcing | wind, heat and freshwater fluxes | ECMWF ERA-Interim 1979-2016 at ¼° 6-hourly
Wave forcing | Hs, Dir, Tp | ECMWF ERA-Interim 1979-2016 at ¼° 6-hourly
Sediment parameters | D50, Ws | Sand: d50=200 microns; Ws=20-50 mm/s Mud (Flocculi): d50=20 microns; Ws=0.03 mm/s
Configuration

## Slide 8: Sediment characteristics (N. Gratiot)
Chart: Concentration (g.L-1)
| 0.01935 | 0.2124 | 0.8919 | 1.0764 | 1.95915 | 1.9659 | 2.731649999999997 | 3.838649999999986 | 4.333333333333372 | 4.333333333333372 | 6.129999999999979 | 6.236000000000018 | 6.899999999999977 | 8.881 | 13.42000000000004 | 15.39999999999992 | 18.10000000000003 | 22.3 | 24.07000000000004 | 28.58000000000003 | 96.5
Ws_surface_médiane | 1.122e-05 | 1.4125e-05 | 0.0001 | 0.0001122 | 0.0001 | 0.00014125 | 0.00019953 | 0.00044668 | 0.00044668 | 0.00063096 | 0.00050119 | 0.00044668 | 0.00050119 | 0.00031623 | 0.00035481 | 0.00050119 | 0.00034674 | 0.00031623 | 0.00035481 | 0.00028184 | 9.5499e-05
Ws_fond_médiane | 3.9811e-05 | 3.1623e-05 | 0.00025119 | 0.00050119 | 0.001122 | 0.00089125 | 0.0017783 | 0.001 | 0.00079433 | 0.00079433 | 0.00056234 | 0.00072444 | 0.00044668 | 0.00039811 | 0.00044668 | 0.00050119 | 0.00017783 | 0.00022387 | 0.00039811 | 0.00019055 | 9.5499e-05
Vmédiane_surface_december | 0.0001 | 1.2589e-05 | 0.0001 | 3.9811e-05 | 3.1623e-05
Vmédiane_bottom_december | 0.00012589 | 3.1623e-05 | 0.00050119 | 7.9433e-05 | 0.00019953
Vmédiane_surface_march | 3.9811e-05 | 1.5849e-05 | 3.1623e-05 | 3.1623e-05 | 1.9953e-05 | 7.0795e-05 | 3.1623e-05 | 0.00014125 | 1.2589e-05 | 1.2589e-05 | 0.00044668 | 1.7783e-05 | 0.00012589 | 6.3096e-05 | 0.00017783
Vmédiane_bottom_march | 0.0039811 | 6.3096e-05 | 0.00019953 | 0.00019953 | 0.00025119 | 3.1623e-05 | 0.0001 | 0.00025119 | 0.00069183 | 0.00039811 | 0.00025119 | 0.0028184 | 0.00015849 | 0.00019953 | 0.00012589 | 0.00031623
Clay
Flocculi
Floc
Sand
For SSC<200mg/l, sediments in LMDCZ can be modeled using 2 types:
Sand
  D50=200 microns
  Ws=20-50 mm/s
Mud (Flocculi)
  D50=20 microns
  Ws=0.03 mm/s
 Erosion parameter and critical shear stress from calibration with satellite data

## Slide 9
Circulation in the ROFI of LMDCZ

## Slide 10: TIDES satellite altimetry data
CTOH group, LEGOS Lab, Toulouse
Joint TOPEX, Jason 1 and Jason 2 tracks of primary mission (green lines) and interleaved mission (black lines) in the Vietnam East Sea (Nguyen et al., 2013)

## Slide 11: Validation with tidal gauges and satellite data
VUNG TAU – July 2009

## Slide 12: Mean currents
January 2014
October 2014

## Slide 13: Salinity
Easily observed and a good tracer of the flow

## Slide 14: Sediment resuspension due to waves

## Slide 15: Sediment resuspension due to waves

## Slide 16: SSC
January
October
MODEL
SAT DATA
January

## Slide 17: SSC
January
October
MODEL
2002-2012 DATA
January
October

## Slide 18: Model erosion
summer
winter

## Slide 19: Sensitivity to river sediment concentration
River sediment concentration decreased from 200 to 50 g/l
SSC Difference

## Slide 20: Sand/Mud fraction tendency
VAST

## Slide 21: CONCLUSIONS
Setup of regional 3D CROCO model done
  Regional oceanic forcing benefits from Hoi-An project and is suitable
  Calibration of sediment models is suitable, using the project’s field surveys and previous observations as well as satellite data
3D modeling includes missing processes in 2D models:
  Salinity fronts and stratification effects
  Cross-shore processes
Sorting out coastal processes will be key to select the right protection measures